How to update F/W of WIZ with 64MB NAND

- Reference

Kernel version 2.6.20

nand filesystem is yaffs2

Frame buffer 240 x 320

Boot& file system are to be updated onto nand flash

While Kernel to be updated onto nor flash

<Pic. 1. WIZ linked to Dev Board>                 developer board

- How to write boot

- Link WIZ and Dev board as shown in <Pic 1>.

Change Jumper of Dev board into UART booting mode.

Insert J9 into LOW of dev board

Put J5 to LOW(power OFF), and then connect to HIGH(power ON)

2) Copy loader.zip file onto pc, and then unzip. Execute DNW onto folder

(program for window)

3) Go to Menu of DNW program. In Configuration, adapt COM PORT to PC environment.

4) In Menu of DNW program, select Serial Port -> UartBoot_16K .

On file selection window, select UART.nb0

< pic 2. UART.nb0 transmission screen  >

5) After transmission is completed, select number 1 when following message appears.

<pic3 menu selection message on terminal>

- On dnw tool, execute Serial Port-> Transmit. And then select NAND.nb0 in file selection window as shown in picture below.

7) After transmission is completed, select number 2 as shown in picture below.

8) After selecting number 2, execute  Serial Port-> Transmit   in dnw tool.

Select  polluxb in file selection window  (=uboot) and then transmit.

9) After transmission is completed, go to item 4 and do actual writing to complete the process. (When “ Image writing done” is displayed on terminal window, it is completed )

11) When all above process are completed, change Jumper back into nand booting mode.

Connect jumper J9 of dev board onto HIGH.

Connect jumper J5 of dev board to LOW(poer OFF) and then connect to  HIGH(Power ON).

The written Boot message shall be loaded on terminal window.

2 Writing: Kernel & Basic File

1) Copy files on following list onto root of SD card .

uImage

uImageUP

update.gz

root.tar.gz

2) Insert SD card into WIZ. Turn it on while pressing R button of WIZ.

Then, Automatic update starts.

3) When automatic update starts, write kernel on nor.

And then Kernel for updating will do booting onto ramdisk file system.

Basic files shall be copied on Nand flash.

4) When following messages are displayed on terminal window, processes are deemed to be completed.

Turn WIZ off and then turn it on. Then WIZ will start actual booting.